## Slide 1: Gear Unit for a Hydronic Valve
Rodenas Tornero, José Miguel – Badpuppet

## Slide 2: Case Description
Input Data
Electric Motor Angular Velocity: 500-1500 RPM
Electric Motor Torque: Graph
Design Space: CAD files
Output Data
Output Shaft Angular Velocity: 1 RPM
Output Shaft Torque: 1 RPM +/- 5%
Radial Rotating Force: Maximum 300 N at tip
Movement: Bi-directional
Hysteresis: <3º
Material: Steel
Shaft Connection: Oldham

## Slide 3: Design Process
Gear Unit Diagram
- Gear Ratio: 523/1
6 z:16
2 z: 15
5 z: 21
7 z: 26
9 z:20
8 z: 17
11 z: 18
Motor N: 523 RPM
3 z: 21
4 z: 15
10 z: 18
1
1
1
1
Planetary Gear System
Arm
N: 1 RPM

## Slide 4: Design Process
6
7
11
8
10
9
2
3
4
5
Gear Unit CAD
Software: SolidWorks
3-4 Shaft x3

## Slide 5: Design Process
Gear Unit CAD
Enclosure Box Changes:
Towers

## Slide 6: Design Process
Assembly
Design Space

## Slide 7: Design Process
Assembly

## Slide 8: Design Process
Assembly

## Slide 9: Design Process
Simulation Study – Strategies for calculating RPM and Torque at output shaft
Output Shaft RPM
Simulation Study
Output Shaft Torque
Output Shaft torque with a frictionless system
Energy losses calculation supposing a 99,0 % of torque transmission per gear contact
Friction between the shaft 5 and the enclosure cover calculation with Simulation Study

## Slide 10: Design Process
Motion Simulation – Preprocess Simulation
Conditions for Output Shaft RPM
Gear Ratios
Electric Motor RPM: 523 RPM
Conditions for Friction Force
Gear Ratios
Electric Motor RPM: 523 RPM
Electric Motor Torque: 0,044 Nm
Axial Force due to helical gears: 991 N
Contact Relation between bodies
Material: Steel (Greasy)
Note: Since the axial force on the shaft 5 is too big, the OldHam connection diameter has been increased. This has been taken into account in the friction simulation study

## Slide 11: Design Process
Motion Simulation – Results
Output Shaft RPM
The solution is exactly 6 deg/s, which is the same as 1RPM
Velocity of the video x0,25

## Slide 12: Design Process
Motion Simulation – Results
Output Shaft Torque
The solution oscillates between 770 and 650 Nmm.
Body1
Body2
Friction Bodies
Axial Force

## Slide 13: Design Process
Motion Simulation – Results
Output Shaft Torque
Perfect Gear Train Torque:
Gear Train with 99% of torque transmission per gear contact:
Friction torque calculated with Motion Simulation: 0,77/0,65 Nm
Output Shaft Torque:

## Slide 14: Design Process
Gear Strenght
Design Method: ISO 6336
Material: Steel – C45 Induction Hardening
Gear ISO Quality: 6
SHP (Contact Strenght): 1372 MPa
SFP (Flexural Strenght): 790 Mpa
Life (Security Factor equal to 1): 2 000 000 cycles
Lubricant viscosity (optional): 150 cSt
KA: 1

## Slide 15: Design Process
2
Gear Strenght - Gear 2
Ft: 466,89 N
mn: 1,00 mm
Z: 15
b: 5,00 mm
i 2-3: 1,40
Cont. Relat. 2-3: 1,35
Helix Direction: Right Hand
αn: 20º
Β: 25º
Inner Diam. : 6,00 mm
XH: 1,06
XF: 2,40

## Slide 16: Design Process
3
Gear Strenght - Gear 3
Ft: 466,89 N
mn: 1,00 mm
Z: 21
b: 5,00 mm
i 2-3: 1,40
Cont. Relat. 2-3: 1,35
Helix Direction: Left Hand
αn: 20º
Β: 25º
Inner Diam. : 6,00 mm
XH: 1,48
XF: 2,53

## Slide 17: Design Process
4
Gear Strenght - Gear 4
Ft: 653,64 N
mn: 1,00 mm
Z: 15
b: 7,00 mm
i 4-5: 1,40
Cont. Relat. 4-5: 1,35
Helix Direction: Right Hand
αn: 20º
Β: 25º
Inner Diam. : 6,00 mm
XH: 1,13
XF: 2,54

## Slide 18: Design Process
5
Gear Strenght - Gear 5
Ft: 653,64 N
mn: 1,00 mm
Z: 21
b: 7,00 mm
i 4-5: 1,40
Cont. Relat. 4-5: 1,35
Helix Direction: Left Hand
αn: 20º
Β: 25º
Inner Diam. : 10,00 mm
XH: 1,60
XF: 2,71

## Slide 19: Design Process
6
Gear Strenght - Gear 6
Ft: 791,23 N
mn: 1,50 mm
Z: 16
b: 5,00 mm
i 6-7: 1,63
Cont. Relat. 6-7: 1,21
Helix Direction: Right Hand (Changed after taken the pictures)
αn: 20º
Β: 35º
Inner Diam. : 6,00 mm
XH: 1,21
XF: 2,30

## Slide 20: Design Process
7
Gear Strenght - Gear 7
Ft: 791,23 N
mn: 1,50 mm
Z: 26
b: 5,00 mm
i 6-7: 1,63
i 7-8: 1,53
Cont. Relat. 6-7: 1,21
Cont. Relat. 7-8: 1,21
Helix Direction: Left Hand (Changed after taken the pictures)
αn: 20º
Β: 35º
Inner Diam. : 6,00 mm
XH: 1,91
XF: 2,34

## Slide 21: Design Process
8
Gear Strenght - Gear 8
Ft: 791,23 N
mn: 1,50 mm
Z: 17
b: 5,00 mm
i 7-8: 1,53
Cont. Relat. 7-8: 1,21
Helix Direction: Right Hand (Changed after taken the pictures)
αn: 20º
Β: 35º
Inner Diam. : 6,00 mm
XH: 1,26
XF: 2,32

## Slide 22: Design Process
9
Gear Strenght - Gear 9
Ft: 663,89 N
mn: 1,75 mm
Z: 20
b: 5,00 mm
i 9-10: 1,11
i 11-9: 1,11
Cont. Relat. 9-10: 1,43
Cont. Relat. 11-9: 1,43
Helix Direction: Right Hand
αn: 20º
Β: 20º
Inner Diam. : 6,00 mm
XH: 1,38
XF: 2,86

## Slide 23: Design Process
10
Gear Strenght - Gear 10
Ft: 663,89 N
mn: 1,75 mm
Z: 18
b: 5,00 mm
i 9-10: 1,11
Cont. Relat. 9-10: 1,43
Helix Direction: Left Hand
αn: 20º
Β: 20º
Inner Diam. : 11,00 mm
XH: 1,25
XF: 2,82
Note: This gear has holes for the screw’s head, so its life will be reduced.

## Slide 24: Design Process
11
Gear Strenght - Gear 11
Ft: 2,59 N
mn: 1,75 mm
Z: 18
b: 5,00 mm
i 11-9: 1,11
Cont. Relat. 11-9: 1,43
Helix Direction: Left Hand
αn: 20º
Β: 20º
Inner Diam. : 6,00 mm
XH: 317,26
XF: 715,12

## Slide 25: Design Process
Axial and Radial Forces
Since helical gears are being used, axial and radial forces appear. We will try to compensate the axial force with the gears of the same shaft, especially on the 3-4-10 group since it’s floating. We will do this changing the helix angle of the gears. Also, the radial force will be compensated by the bearings.

## Slide 26: Design Process
Bearings
Note: Gears 6-7-8 have changed its helix direction to compensate forces
Bearing Type: Angular Contact
Name: ISO 15 ABB - 286 - 10,DE,NC,10_68
N life: 5 000 000 cycles
9 z:20
8 z: 17
351,56 N
554,03 N
257,14 N
241,64 N
154,37 N
454,34 N
795,66 N

## Slide 27: Design Process
Bearings
Radial forces are not collinear, but its effect is negligible.
Bearing: Radial Ball Bearing
Name: ISO 15 RBB - 286 - 10,DE,NC,10_68
N life: 5 000 000 cycles
7 z: 16
554,03 N
554,03 N
351,56 N
351,56 N
-
-

## Slide 28: Design Process
Bearings - Reactions
Bearing: Radial Ball Bearing
Name: ISO 15 RBB - 286 - 10,DE,NC,10_68
N life: 5 000 000 cycles
6 z:16
2 z: 15
The moment is compensated by the 3-4 shafts. This will cause a small disbalance of the tangential forces, which causes a small error in the gear strength calculation.
554,03 N
351,56 N
653,13 N
425,41 N
99,12 N

## Slide 29: Design Process
Bearings - Reactions
Note: That is the axial force of each shaft, the total axial force would be 3x 87,09 N
Bearing Type: Angular Contact
Name: ISO 15 ABB - 286 - 10,DE,NC,10_68
N life: 5 000 000 cycles
3 z: 21
4 z: 15
217,71 N
304,80 N
187,50 N
262,50 N
220,64 N
87,09 N
229,36 N

## Slide 30: Design Process
Bearings - Reactions
3 z: 21
4 z: 15
10 z: 18
The axial force is compensated by the friction between gears
257,14 N
241,64 N
653,13 N
914,40 N
19,62 N

## Slide 31: Design Process
Hysteresis at shaft 5
The three 3-4 shaft compensates its radial forces, so the radial force at shaft 5 will be caused by the gear 10 and the gear 6.
6 z:16
2 z: 15
5 z: 21
3 z: 21
4 z: 15
10 z: 18
1
1
257,14 N
351,56 N
425,41 N
183,19 N
8 mm
14 mm
35 mm
183,19 N

## Slide 32: Design Process
Hysteresis at shaft 5
Preprocess Simulation:
Material: Steel

## Slide 33: Design Process
Hysteresis at shaft 5
A displacement of 3º would be 1 mm. In our case, the hysteresis is 2,843e-03 º